## Slide 1
DIGITAL DESIGN PROJECT
8-bit Register
with Load Enable
A D flip-flop based circuit that loads new data on command and holds its value otherwise
Design • Operation • Logic • Applications
Notes: Introduce the project. An 8-bit register stores one 8-bit word. The Load Enable input decides whether the next active clock edge stores new input data or keeps the previous word. The design uses D flip-flops, one per bit.

## Slide 2
Project goal and design specification
02
Build a storage block that can update on command and retain its value between updates.
Width
8 bits: D7–D0 and Q7–Q0
Control
EN = 1 loads input data; EN = 0 holds the stored word
Timing
Synchronous: the register changes only at the active clock edge
Storage
Eight D flip-flops, one for each bit
No reset input is specified in the project prompt
Notes: The input word D[7:0] carries the value to store. The output word Q[7:0] is the value currently held. EN is a control signal. The design prompt does not mention reset, so this design focuses on load and hold. Without a reset, the power-up value is not guaranteed.

## Slide 3
One bit: the building block
03
Each bit needs a choice between new data and its own old value.
2:1 MUX
select = EN
D FLIP-FLOP
stores one bit
Dᵢ
selected value
Qᵢ (stored bit)
feedback: keep the old value when EN = 0
EN
CLK ↑
New data
The MUX chooses what the flip-flop receives at its D input.
Notes: Explain the one-bit cell. A 2-to-1 multiplexer has two data choices. One choice is external input D_i. The other is the flip-flop output Q_i, routed back as feedback. EN controls the choice. The selected value reaches the D input of the flip-flop. The flip-flop captures that value only at the active rising edge of CLK.

## Slide 4
Eight bits share one enable and one clock
04
Repeat the one-bit cell eight times to store a complete byte.
INPUT
MUX
D FLIP-FLOP
OUTPUT
D7
MUX 7
DFF 7
Q7
D6
MUX 6
DFF 6
Q6
D5
MUX 5
DFF 5
Q5
D4
MUX 4
DFF 4
Q4
D3
MUX 3
DFF 3
Q3
D2
MUX 2
DFF 2
Q2
D1
MUX 1
DFF 1
Q1
D0
MUX 0
DFF 0
Q0
Shared controls
EN drives all MUX select pins.
CLK drives all flip-flops.
Each Qᵢ feeds back to its own MUX.
8 MUXes + 8 D flip-flops
Notes: The eight MUX and D flip-flop pairs form eight parallel bit slices. The D7 input goes to bit 7, and so on through D0. Each Q output feeds back only to its own MUX. All slices use the same EN signal and the same clock, so the full 8-bit word loads together.

## Slide 5
The load-enable rule
05
For each bit i, the next state is:
Qᵢ(next) = EN · Dᵢ + EN̅ · Qᵢ(current)
The equation describes the MUX output before the clock edge.
EN
Dᵢ input
Qᵢ(next)
0
Any
Qᵢ(current)
1
Dᵢ
Dᵢ
EN = 0 selects feedback. EN = 1 selects new input data.
· means AND
A·B is 1 only when both A and B are 1.
+ means OR
The two terms cannot both be selected at once.
Notes: Read the equation aloud. If EN is zero, the first term is zero and EN-bar is one, so Q next equals current Q. If EN is one, EN-bar is zero, so Q next equals D. This is the Boolean form of a 2-to-1 MUX. The flip-flop takes Q(next) at its active clock edge.

## Slide 6
The clock decides when the value changes
06
EN controls what will be stored. The active clock edge controls when it is stored.
Clock event
EN
D input
Q before edge
Q after edge
Rising edge 1
1
10110110
unknown / prior
10110110
Rising edge 2
0
00111100
10110110
10110110
Rising edge 3
1
00111100
10110110
00111100
Between active edges, Q remains stable
Assumption: positive-edge triggered D flip-flops
Notes: This project assumes positive-edge-triggered D flip-flops, shown by the rising-edge symbol. Inputs can change between clock edges, but the stored Q output does not change until the next rising edge. At that edge, EN selects whether the register loads or holds. The first row says unknown/prior because there is no reset in the specified circuit.

## Slide 7
Worked example: load, hold, then load again
07
Track the complete 8-bit word at each rising edge.
Moment
EN
D[7:0]
Q[7:0]
Before edge 1
—
—
not specified
After edge 1
1
10110110
10110110
After edge 2
0
00111100
10110110
After edge 3
1
00111100
00111100
Edge 1 stores. Edge 2 holds. Edge 3 stores the new word.
Notes: Walk through the table. On edge 1, EN=1, so the register captures 10110110. Before edge 2, D changes to 00111100, but EN=0, so the Q output stays 10110110. At edge 3, EN returns to 1 and the new word is captured. Emphasize that merely changing D does not alter Q.

## Slide 8
Logisim implementation plan
08
1
Place eight D flip-flops
Use one storage element for each bit.
2
Place eight 2:1 MUXes
Put one MUX before each flip-flop input.
3
Wire each bit slice
MUX inputs are Dᵢ and feedback Qᵢ; MUX output goes to D of its flip-flop.
4
Share EN and CLK
Connect the same enable and clock to all eight slices.
5
Check both modes
EN=1 loads; EN=0 holds the previous 8-bit output.
Notes: When building in Logisim, make sure the MUX select pin is connected to EN and each flip-flop clock pin receives the same clock. A common mistake is to connect the feedback from one bit to a different bit. Test the circuit first with EN=1, then change D while EN=0 and check that Q holds.

## Slide 9
Where load-enable registers are used
09
Processor registers
Hold operands, addresses, or intermediate results until a control signal permits an update.
Pipeline stages
Keep a stage’s data stable when the next stage is not ready to accept it.
Input and output buffers
Capture a data word at a chosen clock edge and present it steadily to another block.
Controlled data storage
Update a stored word only when a write or load condition is active.
The shared idea: store a word, update it selectively, and preserve it otherwise.
Notes: Give these as examples of the same circuit pattern. The exact design and control conditions differ between systems, but the load-enable behavior is useful whenever a block must retain its current word until an update is allowed.

## Slide 10
Key points to explain in a viva
10
1
Eight D flip-flops store one 8-bit word.
2
A MUX before each flip-flop chooses new data or feedback.
3
EN = 1 loads D[7:0] at the next rising edge.
4
EN = 0 feeds Q back, so the stored value is held.
5
All bits update together because the clock is shared.
Core rule
Q(next) = EN·D + EN̅·Q(current)
Notes: Close by explaining the rule in your own words: the enable selects the next value, and the clock edge stores it. If EN is high the new data enters the register. If EN is low the output is routed back and remains unchanged. The equation is applied independently to all eight bits.